## Slide 1
REVIEW 3 · METHODOLOGY DEVELOPMENT
AquaWatch — Real-Time Water Quality Monitoring for Rural Drinking Water Sources
Presented by:
2510040070 - Sania Khan
2510040083 - P.Srija
2510040109 - K.Sravya
2510040120 - B.Gowri

## Slide 2
Methodology Overview
AquaWatch follows an iterative hardware-software co-design process, moving from system design through build, integration, and validation.
1
System Design
Define architecture, select components, and design the data flow end to end.
2
Hardware Development
Assemble and wire the ESP32 with pH, turbidity, and TDS sensors.
3
Software Development
Build firmware, cloud integration, and the live dashboard.
4
Testing & Validation
Calibrate, integrate, and verify accuracy against reference methods.
AquaWatch | Review 3 — Methodology Development
2

## Slide 3
System Design & Architecture
The system is organized into four functional layers, each handling one stage of the data pipeline.
1
Sensing Layer
pH, turbidity, and TDS probes take continuous analog readings from the water source.
2
Processing Layer
ESP32 microcontroller reads raw signals, applies calibration formulas, and checks safe-range thresholds.
3
Communication Layer
Readings are published over MQTT; a Node.js backend subscribes and bridges them to clients over WebSocket (Socket.io).
4
Application Layer
React dashboard receives the live WebSocket stream and renders charts and alerts.
AquaWatch | Review 3 — Methodology Development
3

## Slide 4
Hardware Development Methodology
Stage | Activity
Component Selection | Choose ESP32 for built-in WiFi and analog inputs; select pH, turbidity, and TDS sensor modules compatible with 3.3V analog input
Circuit Design | Design signal-conditioning circuitry (voltage dividers, filtering) so each sensor's output maps cleanly to the ESP32's ADC range
Enclosure Design | House the ESP32 and wiring in a sealed enclosure; route sensor probes through cable glands to the outside
Assembly & Wiring | Assemble on breadboard first for testing, then transfer to a soldered/perfboard build for the final unit
AquaWatch | Review 3 — Methodology Development
4

## Slide 5
Software Development Methodology
Built and tested in three layers, developed iteratively so each layer can be verified before the next depends on it.
1
Firmware (ESP32)
Modular functions for each sensor; calibration constants applied to raw readings; threshold logic determines alert state; readings packaged as JSON and published to an MQTT topic.
2
Backend (Node.js + MQTT)
Node.js server subscribes to the MQTT broker, bridges live readings to connected clients over WebSocket (Socket.io), and persists historical readings in PostgreSQL/TimescaleDB.
3
Frontend (React)
Custom hook subscribes to the WebSocket stream; Chart.js renders time-series graphs; component structure separates stat display, charts, and alerts.
AquaWatch | Review 3 — Methodology Development
5

## Slide 6
Testing & Validation Methodology
Verification happens at four levels, from individual sensors up to the full pipeline.
1
Unit-Level Testing
Each sensor is tested individually against known reference/buffer solutions to verify its calibration formula.
2
Integration Testing
Full pipeline is run end to end — sensor to dashboard — to check data accuracy and update latency.
3
System Stability Testing
The assembled unit runs continuously over several days to check for drift, disconnects, or missed readings.
4
Comparative Validation
Readings are cross-checked against a manual test method (e.g., a Field Test Kit) on the same water sample.
AquaWatch | Review 3 — Methodology Development
6